## Slide 1: Smart LPG Gas Leakage Detection
ESP32 Mini Project

## Slide 2: Objectives
Detect LPG gas leakage.
Display system status on an LCD.
Alert users using a buzzer.
Automatically close the gas valve using a servo motor.
Turn ON an exhaust fan using a relay.Improve household and industrial safest

## Slide 3: Components
ESP32 Development Board
MQ-2 Gas Sensor
SG90 Servo Motor
16×2 I2C LCD
Relay Module
Active Buzzer
Buck Converter
Breadboard
Jumper Wires
Power Supply.

## Slide 4: CIRCUIT CONNECTION
COMPONENTS | GPIO
MQ-2 | GPIO-34
SERVO | GPIO-13
BUZZER | GPIO-26
RELAY | GPIO-27
LCD SCL | GPIO-22
LCD SDA | GPIO-21

## Slide 5: Working
Normal Condition
MQ-2 continuously monitors gas.
LCD displays LPG SAFE.
Servo remains at 0°.
Relay OFF.Buzzer OFF.
Gas Leakage
MQ-2 detects LPG.
ESP32 activates the buzzer.
Relay turns ON.
Servo rotates to close the gas valve.
LCD displays WARNING! GAS LEAK.

## Slide 6: BLOCK DIAGRAM
LPG Gas │MQ-2 Sensor │ESP32 Controller ├─────────────┬──────────────┬─────────────┐ │ │ │ │LCD Buzzer Relay Servo │ Exhaust Fan

## Slide 7: FLOWCHART
Start
↓
Initialize ESP32
↓
Read MQ2 Sensor
↓
Gas > Threshold ?
↓
YesLCD Warning
↓
Buzzer ON
↓
Relay ON
↓
Servo 90°
↓
Continue Monitoring
↓
No
↓
LCD Safe
↓
Relay OFF
↓
Servo 0°
↓
Repeat

## Slide 8: Advantages
Low-cost system
Easy to build
Automatic safety response
Reduces fire hazards
Easy to upgrade with IoT
User-friendly
LCD interface
Suitable for homes and industries

## Slide 9: Future Scope
Future Enhancements
Blynk IoT mobile notifications
GSM SMS alerts
Flame sensor integration
Temperature monitoring
Cloud data logging
AI-based gas level prediction
Battery backup
Mobile application